## Slide 1: SecNDP: Secure Near-Data Processing with Untrusted Memory
Wenjie Xiong∗§, Liu Ke∗†§, Dimitrije Jankov‡, Michael Kounavis∗,
Xiaochen Wang∗, Eric Northup∗, Jie Amy Yang∗,
Bilge Acun∗, Carole-Jean Wu∗, Ping Tak Peter Tang∗,
G. Edward Suh∗⋄, Xuan Zhang†, Hsien-Hsin S. Lee∗
∗Meta, †Washington University in St. Louis,
‡Rice University, ⋄Cornell University
§The first two authors contributed equally to this work

## Slide 2: “Memory Wall”
Performance Bottleneck
CPU
Power
…
Source: https://medium.com/riselab/ai-and-memory-wall-2cb4265cb0b8
The scaling of the bandwidth of different generations of interconnections & Memory, as well as the Peak FLOPS. As can be seen, the bandwidth is increasing very slowly

## Slide 3: “Memory Wall” and Near Data Processing (NDP)
…
NDP
PU
Performance Bottleneck
NDP
PU
CPU
CPU
Power
1.Parallel accesses
~4x end-to-end speedup for recommendation models
2.Power-saving
20% less power for recommendation models
NDP Example
…
Near-Data
Processing (NDP)
Processing Unit (PU)

## Slide 4: CPU TEEs Today
…
NDP
PU
CPU
NDP
PU
Cold Boot Attack
Backdoor/Trojan
Information Leakage!
Encryption Engine
Security boundary
Trusted Execution Environment (TEE) provides strong confidentiality and integrity protection using hardware.
CPU TEEs has become a mature technology (e.g., Intel SGX, AMD SEV, ARM TrustZone/CCA, IBM SecureBlue++, RISC-V KeyStone)
Threat model:
  The main processor (CPU TEE) is trusted.
  Memory (including NDP PU) is untrusted.
CPU TEE
Bus Snooping
Trusted
Untrusted

## Slide 5: CPU TEEs Today
…
NDP
PU
CPU
NDP
PU
Encryption Engine
Security boundary
CPU TEE
Trusted
Untrusted
Off-chip data is protected by encryption.
Current memory encryption does not support computation over ciphertext, hindering the adoption of NDP techniques.
Encrypted
ciphertext
NDP cannot operated on encrypted data.
“SecNDP”

## Slide 6: Contributions of SecNDP
…
NDP
PU
CPU
NDP
PU
Bus Snooping
Cold Boot Attack
Backdoor/Trojan
Information Leakage!
Encryption Engine
Security boundary
Following the threat model of CPU TEEs, to enable secure NDP with untrusted memory:
We proposed an encryption scheme allow computation over ciphertext in the untrusted NDP.
We proposed an integrity verification scheme to validate the correctness of the computation in NDP.
The schemes demonstrate performance approaching to that of unprotected NDP.
CPU TEE

## Slide 7: Outline
Motivation
  Near Data Processing (NDP)
  CPU TEEs and its threat model
SecNDP Scheme
  SecNDP Encryption
  SecNDP Verification
  SecNDP Architecture design
SecNDP Performance Evaluation
  Evaluation Method
  Evaluation Results
Conclusions

## Slide 8: Background: Arithmetic Secret Sharing in secure Multi-Party Computation
Random
,
Untrusted
Worker 1
Untrusted
Worker 2
To compute:
Client
,
NDP
PU
Untrusted Memory
MPC protects confidentiality from an untrusted party.
CPU
Encryption Engine
CPU TEE
However, existing MPC scheme assume each party will use the same amount of computing resources and memory.
The sum of the shares is the original plaintext data.
With only one share of secret, the untrusted worker cannot recover the original secret.
Notes: upfront
This is an example of 2-party MPC
Comment on the security in the begining.

## Slide 9: Background: TEE Memory Counter-Mode Encryption
Untrusted Memory
Plaintext
data
OTP takes the address and a version number as inputs.
On-chip AES engines can generate OTP efficiently in parallel with memory accesses.
NDP
PU
Encryption (in the processor)
a.k.a., “One time pad (OTP)” or “encrypted counter” using a block cipher
Notes: remove counter-mode
add animation

## Slide 10: SecNDP Encryption
Untrusted Memory
Plaintext
data
OTP takes the address and a version number as inputs.
On-chip AES engines can generate OTP efficiently in parallel with memory accesses.
NDP
PU
Encryption (in the processor)
a.k.a., “One time pad (OTP)” or “encrypted counter” using a block cipher
Like the arithmetic secret-sharing in MPC, the sum of OTP and ciphtertext is the plaintext data.
We can do computation over !
Notes: remove counter-mode
add animation

## Slide 11: Computation using SecNDP
Untrusted Memory
To compute:
Plaintext
NDP
PU
(in the processor)
AES
1. Generate OTP
2. Computation on OTP
3. Adding results
Parallel accesses
Save memory traffic
ADD/MUL
ADD/MUL
Computation on ciphertext
(compute-intensive)
No memory access required
(memory-intensive)
Notes: add animation

## Slide 12: On the Security of SecNDP Encryption
SecNDP
distinguishing advantage associated with the invoked cipher, e.g., AES
denominator is the number of all
possible key values
Notes: add animation

## Slide 13: Outline
Motivation
  Near Data Processing (NDP)
  CPU TEEs and its threat model
SecNDP Scheme
  SecNDP Encryption
  SecNDP Verification
  SecNDP Architecture design
SecNDP Performance Evaluation
  Evaluation Method
  Evaluation Results
Conclusions

## Slide 14: TEE Memory Integrity Protection
Plaintext
data
NDP
PU
Encryption and Verification (in the processor)
a.k.a., “One time pad (OTP)” or “encrypted counter” using a block cipher
AES/Ver
One-way hash function
Generate integrity tag for
retrieve data and tag
Untrusted Memory
Current memory integrity protection cannot verify the correctness of computation results.
Notes: remove counter-mode
add animation

## Slide 15: Verifying Linear Operations f(x) using SecNDP
A linear hash function () can be used to verify linear operations (). =
The linear hash is encrypted using SecNDP encryption. The untrusted memory can compute .
Untrusted Memory
NDP
PU
Encryption and Verification Tag Generation (in the processor)
AES/Ver
a.k.a., “One time pad (OTP)”
Verification tag
for each vector
Linear hash function (Ver)
Generate verification tag for
Plaintext
data
,
, where is a matirx
= ))

## Slide 16: Verifying Linear Operations using SecNDP
,
Untrusted Memory
To compute:
Plaintext
NDP
PU
Decryption and Verification (in the processor)
1. Generate “one time pad” (OTP) and their tags
2. Computation on OTP and verification tags
3. Adding results and verify the results
Verification tag
for each vector
AES
ADD/Ver
ADD/MUL
ADD/MUL
Computation on ciphertext
The CPU and NDP compute the resulting verification tag jointly through secret sharing.
The verification tag is compared with the hash of the computation result.

## Slide 17: On the Integrity of Linear Operations
distinguishing advantage terms associated with the invoked ciphers
number of matrix
columns
large prime number
involved in integrity computations
i.e., size of verification tag, ​
e.g., 2127-1​

## Slide 18: Verification Tag Storage
… |  |  |  |  |  |  | 
1) Ver-coloc
2) Ver-sep
3) Ver-ECC
In DRAM reserved for error correction code (ECC)
Encrypted data
Verification tag
Pros: Consecutive memory access for data and tags
Cons: Need to Allocate memory in application software
Pros: Do not change memory layout of data
Cons: Separate memory access for embedding entry and tag
Pros: no extra memory access for tags
Cons: Still need to access ECC if verification fails

## Slide 19: Outline
Motivation
  Near Data Processing (NDP)
  CPU TEEs and its threat model
SecNDP Scheme
  SecNDP Encryption
  SecNDP Verification
  SecNDP Architecture design
SecNDP Performance Evaluation
  Evaluation Method
  Evaluation Results
Conclusions

## Slide 20: SecNDP Architecture Design
SecNDP engine:
  AES engine
  OTP PU
  Verification engine
One addition on the memory critical path for confidentiality protection.
ISA extension for SecNDP is described in the paper.
Core
L1/L2
…
Memory Controller
Core
L1/L2
LLC
Offloading
NDP packets
NDP-DIMM
NDP-DIMM
NDP-Cmd
NDP-extension
DRAM access
NDP PU
NDP-Cmd
Rank0.NDP-Cmd
Rank1.NDP-Cmd
Rank-NDP PU
Rank-NDP PU
SecNDP Engine
TLB
TLB
Security Boundary = processor
Req. buf.
AES Engine
AES Engine
from cache
to mem
dec.
buf.
Req. buf.
Resp. buf.
Enc?
OTP PU
+
Resp. buf.
…
Y: addr, v
to cache
from mem
Op, we
e, we
Veri.
CPU Inst:
NDPInst, NDPLd
Reg.
DRAM
DRAM
DRAM
DRAM
DRAM
DRAM
DRAM
DRAM
ArthEnc, SecNDPInst, SecNDPLd
Blue: NDP
Green: SecNDP

## Slide 21: SecNDP Architecture Design - ISA
ISA extension
  Version number (v) is needed for SecNDP protection
  Optional verification (Veri?)
cmd
Daddr
NDP Op
ACT/RD/PRE | Rank, BG, BA, Row, Col | Add/Mul | vsize | dsize | Imm | RegID
NDP-Cmd:
we
m
ai
paddr(Pi)
Mul
dest
Add/Mul | vsize | dsize | Imm | NDPRegID | addr | v | veri?
SecNDPInst:
vsize | dsize | addr | v | veri?
ArthEnc:
Add/Mul | vsize | dsize | Imm | NDPRegID | addr
NDPInst:
CPU Inst:
NDPRegID
NDPLd:
NDPRegID | veri?
SecNDPLd:
Blue: NDP
Green: SecNDP

## Slide 22: Life Cycle of SecNDP Execution
Ei
CTi
res = Cres + Eres mod 2we
CTres=
Eres=
Cres=
ETi
ETres=
Tres = hK(res)
Tres = CTres+ETres mod q?pass:fail
Verification (Optional)
Processor (TEE)
meta-data trans.
 | ai | 
 | ai | 
 | ai | 
 | ai | 
Encryption Engine
data trans.
T0. init.
Ci
Pi
Encryption Engine
T1. Computation (Query a)
CTi
Ci
addr,v
ArthEnc
SecNDPInst
(compute-intensive)
(memory-intensive)
SecNDPLd
Example: Vector and Matrix Multiplication (a x P)

## Slide 23: Outline
Motivation
  Near Data Processing (NDP)
  CPU TEEs and its threat model
SecNDP Scheme
  SecNDP Encryption
  SecNDP Verification
  SecNDP Architecture design
SecNDP Performance Evaluation
  Evaluation Method
  Evaluation Results
Conclusions

## Slide 24: Experimental Methodology
Workloads:
  Deep Learning Recommendation Model (RMC in the table)
    Embedding table lookups: memory-intensive, executed in NDP
    Fully connected layers: compute-intensive, executed in the CPU TEE
  Medical Data analytics, e.g., sum: memory-intensive, executed in NDP
Simulation setup
  In-house NDP simulator
    Memory: DDR4, using on Ramulator
    SecNDP engine: use the performance results of AES Engine in [22]
CPU TEE baseline:
  Intel SGX on CoffeeLake, 168MB SGX EPC, with integrity protection
  Intel SGX on IceLake, 96GB SGX EPC
Notes: Compare with SGX
Add box to highlight the comparison

## Slide 25: Performance Evaluation of SecNDP
With enough AES engines, SecNDP's system performance is close to unprotected NDP while providing data confidentiality and integrity guarantee.
More performance analysis of SecNDP with different number of AES engines and different verification tag storage methods in the full paper.
Existing CPU TEE
End-to-end speedup, with 8 NDP PUs.
Notes: Compare with SGX
Add box to highlight the comparison

## Slide 26: Accuracy of Integer Operation
Like in MPC, we only support integer and fixed-point operations in SecNDP.
The accuracy results suggest that SecNDP maintains the desired model accuracy requirement.

## Slide 27: Power Consumption
The pooling factor (PF) denotes the level of data aggregation, i.e., the ratio of the raw data size to the size of the computed result.
When pooling factor PF=80, SecNDP saves memory system energy by 18% with encryption-only mode and by 8% with verification.

## Slide 28: Conclusions
…
NDP
PU
CPU
NDP
PU
Encryption Engine
Security boundary
SecNDP is the first work to enable a TEE in the presence of untrusted memory to leverage the performance and energy benefits of NDP securely.
  We proposed an encryption scheme allow computation over ciphertext in the untrusted NDP.
  We proposed an integrity verification scheme to validate the correctness of the computation in NDP.
SecNDP schemes demonstrate performance approaching to that of unprotected NDP.
  Performance (7.46x speedup)
  Energy consumption (18% energy-saving)
  Accuracy (negligible impact)
CPU TEE
Thank you!